## Slide 4
Is a device that stores energy by maintaining a separation between positive and negative charge.
Compare stored energy / charge to a bucket of water which can be filled and emptied.
Consists of two conductors (metal) separated by an insulator.
Capacitors have many applications:
Computer keyboards
Electronic flashes for cameras
Electric power surge protectors
Radios and electronic circuits
(Symbol: )
Capacitor

## Slide 6: capacitors

## Slide 11
Q and V are proportional:
Q = C V
C = Capacitance
(a fixed property of each capacitor)

## Slide 12
SI unit = 1 Farad (F)
i.e. 3μF = 3*10-6 F
When the capacitor is fully charged:
the current flow stops
both plates have an equal and opposite amount of charge Q
the pd across the plates, V = the supply voltage
a uniform electric field exists between the plates

## Slide 13
A
1) A = plate area
d
2) d = plate separation
3) Adding a dielectric
εr = dielectric constant
C  A
C  1/d
The capacitance of a parallel capacitor depends on 3 factors
εo is the absolute permittivity of free space
(0= 8.85 x 10-12 C2/Nm2)
Adding a dielectric increases the Capacitance

## Slide 14
17.8 Dielectrics
The molecules in a dielectric tend to become oriented in a way that reduces the external field.
The dielectric blocks some of the electric field lines, so the voltage decreases. Since Q=CV, if V decreases, C increases. Q must stay constant because the capacitor is not connected to a voltage source.

## Slide 15
17.8 Dielectrics
This means that the electric field within the dielectric is less than it would be in air, allowing more charge to be stored for the same potential.

## Slide 16
Determine C

## Slide 17
Determine Q

## Slide 18
Determine C & V
with εr = 5.0

## Slide 19
A porcelain dielectric is placed between the plates.
What is the value of the new capacitance?
Capacitors
distance | metres
cm | 1 x 10-2
mm | 1 x 10-3
µm | 1 x 10-6
nm | 1 x 10-9
pm | 1 x 10-12
100 mm
12 mm
4.0 mm
Show the area of the capacitor plate is 48 mm2; and
determine the value of the capacitor.
DIELECTRIC CONSTANT OF MATERIALS |  |  |  |  | 
Air | 1.00 | Cellulose | 3.70 | Glass | 7.75
Teflon | 2.10 | Fiber | 6.00 | Mica | 5.40
Paper | 3.00 | Porcelain | 5.57 | Quartz | 3.80

## Slide 20
A
A porcelain dielectric is placed between the plates.
What is the value of the new capacitance (Cd)?
Capacitors
100 mm
12 mm
4.0 mm
M
M
Show the area of the capacitor plate is 48 mm2.
determine the value of the capacitor.