## Slide 1
Unless stated otherwise all AC voltage & current values are rms values
“RC” - AC circuits

## Slide 2
ngsir.netfirms.com/englishhtm/RC_dc.htm

## Slide 4
XC is the ‘Reactance’ of the capacitor, unit ohm (Ω)
Reactance is the property of a capacitor to limit AC current in a circuit.
Similar to resistance but is affected by the frequency of the AC supply
larger C means more q stored so more I flow
Greater f means q is moving on & off the plates at a greater rate ie higher I

## Slide 5
Unless stated otherwise all AC voltage & current values are rms values

## Slide 6
AC supply
VS
VC
VR
For the above circuit the following voltages were measured:
VR = 6.0 V
VC = 8.0 V
VS = 10.0 V
VS =14.0 V ?
Voltages across R & C are out of phase…
Unless stated all AC voltage & current values are rms values

## Slide 7
The phase relationship between VC & VR
Out by ¼ of a cycle or 90o
Phasors are rotating anticlockwise, VR is always 90o ahead of VC at any time
“ the resistor voltage is leading the capacitor voltage by 90o”
AC supply
VS
VC
VR
Why? – 160

## Slide 8
2 R & I Phasors Applet

## Slide 9
See 3 C & I Phasors applet

## Slide 10
See 4 RC circuits applet

## Slide 11
For components in series VS = VC + VR
To get VS add VC & VR phasors as vectors
Current is in phase with the resistor voltage
Voltage relationship between VS, VC & VR

## Slide 12
Impedance
Resistance & reactance both impede the flow of current in a circuit. There combined effect is called impedance, symbol Z, unit Ω
Combining the voltages gives:

## Slide 13
2
This RC circuit comprises of a 2,400 µF capacitor and a 2.0 Ω resistor and a 50 Hz power supply.
Calculate the reactance of the capacitor.
Draw a phasor diagram and determine the impedance of the circuit.
RC circuit
R = 2.0 Ω
XC = 1.3 Ω
Z = 2.4 Ω
R =2.0 Ω
C = 2,400 µF
50 Hz
1

## Slide 14
RC circuit
This RC circuit comprises of a 2,400 µF capacitor, a 2.0 Ω resistor and a 50 Hz power supply.
The current in the circuit 4.2 A
The reactance XC of the capacitor is 1.3 Ω.
Calculate the potential drop across the capacitor (VC) and the potential drop across the resistor (VR)
Determine the supply voltage (VS)
Determine the phase difference between the current and the supply voltage (VS)
Label the waves on the graph with VR, VC and VS.
R =2.0 Ω
C = 2,400 µF
50 Hz

## Slide 15
2
RC circuit
This RC circuit comprises of a 2,400 µF capacitor, a 2.0 Ω resistor and a 50 Hz power supply.
The current in the circuit 4.2 A
The reactance XC of the capacitor is 1.3 Ω.
Calculate the potential drop across the capacitor (VC) and the potential drop across the resistor (VR)
R =2.0 Ω
C = 2,400 µF
50 Hz
Both correct
2. Determine the supply voltage (VS)
VC = 5.5 V
VR = 8.4 V
θ
VS = 10 V
VS lagging current by 31º ± 2º
31º ± 2º only
3. Determine the phase difference between the current and the supply voltage (VS)
By measurement or by calculation

## Slide 16
Formative practice enables students to gain frequent feedback and feedforward on the progress of their education
VR
VC
VS
31º
Further Explanation
Reference circles not required for answer
VR
VC
VS
4. Label the waves on the graph with VR, VC and VS.
RC circuit
R =2.0 Ω
C = 2,400 µF
50 Hz

## Slide 17
C
R
120 V
60 Hz
R = 25 W
C = 30 mF
What is the phase angle (between Vs and I) of the circuit shown in the diagram?
Problem
R
XC
Z
f