## Slide 3: Calculating the magnetic field strength around a current carrying wire:
d
B= Magnetic field strength [T]
I = Current [A]
d = Distance [m]
Right hand screw rule
fingers ~ field
Thumb ~ current

## Slide 4
dot is coming out of the page
cross is going into the page
Since it’s difficult to draw in 3-D, adopt the following symbols:

## Slide 8
Bend a straight current carrying wire into a loop and investigate the field

## Slide 9: Right Hand Rule (solenoid)
If you wrap your fingers around the coil in the direction of the current, your thumb points north.
Thumb points to N
Fingers curl with I

## Slide 10
See Solenoid applet

## Slide 11
A solenoid is a long coil of wire. If it is tightly wrapped, the magnetic field in its interior is almost uniform:
B α nI

## Slide 12
the magnetic field strength of a solenoid is directly related to the current through the coil.
the number of turns of wire around a solenoid is directly related to the magnetic field strength of the solenoid.
This solenoid has a soft iron core which is more permeable and as a result, creates a much stronger magnetic field. As a result, it is a much stronger electromagnet.

## Slide 13: a stronger field round a solenoid
the field can be made stronger by:
using an iron core
using more turns of wire
increasing the current

## Slide 15
The electric bell below uses an electromagnet to make it work.
When the bell push, A, is closed, electric current can flow through the coil and the electromagnet, B, attracts the hammer, D.
The hammer is connected to a contact, C, and as the hammer moves it breaks the circuit and the electricity stops flowing. The springy metal, E, pulls the hammer back into its position.
This image and text came from
www.bbc.co.uk/.../ physics/electromag2_5.shtml