## Slide 1
NCEA 2007

## Slide 2: LR Time Constant
As with Capacitors, if an Inductance is connected in series with a resistor then there is delay in obtaining the full current/voltage.
Decay of Current in Inductor
Time
I = V/R
t
Growth of Current in Inductor
Time
Final steady state current
I = V/R
t
L
R
V

## Slide 3
IR
Vs
x
y
VL
I
RL Circuits
Switch to X, I increases from 0 to Imax. While I is increasing Inductor VL acts against the supply voltage Vs. At any moment: Vs – IR – VL=0 (loop rule)
At t = 0+, the current is just starting to flow, but there is still negligible voltage drop across resistor
Vs – IR – VL=0
Vs – 0 – VL=0
Vs = VL= L ΔI/Δt
Time constant t = L/R
t = time taken for a change of 63%

## Slide 4
t = L/R
For t >> t (ie 5 t) Assume Imax
No change in current through inductor, VL in inductor is 0.
Vs – IR – VL=0
Vs– IR – 0 = 0
I = Vs /R
Current in the circuit…

## Slide 5
IR
Vs
x
y
VL
I
Switch to y, I decreases from steady Imax to 0. While I is decreasing Inductor VL acts to prevent current fall. At any moment: VL- IR = 0 (loop rule)

## Slide 7
Chart: 
Calculate the time constant t , L = 750 mH
Show on the graph the coordinate (t, VL)
3. a) Calculate Imax
b) Sketch the current vs time graph for the above circuit.
c) On your graph show the coordinates with values of Imax, t and VL.
A voltage VL vs time t graph of an inductor in a DC circuit when the switch is closed.
12
9
6
3
0
t (s)
VL (V)
Inductor
VS
3 Ω
Vs
switch
L = 750 mH
VL

## Slide 8
Chart: 
Calculate the time constant t , L = 750 mH
12
9
6
3
0
t (s)
VL (V)
Inductor
VS
3 Ω
Vs
switch
L = 750 mH
VL
2. Show on the graph the coordinate (VL, t)
4.4
t
VL = VS e-1
VL = 37% x VS
VL = 4.4 V
A voltage VL vs time t graph of an inductor in a DC circuit when the switch is closed.

## Slide 9
Chart: 
4
3
2
1
0
2.5
t
I (A)
t (s)
3 Ω
Vs
switch
L = 750 mH
VL
3. a) Calculate Imax
b) Sketch the current vs time graph for the above circuit.
Imax = V ÷ R
Imax = 12 ÷ 3 \ Imax = 4 A
Imax
c) On your graph show the coordinates with values of Imax, t and VL.

## Slide 10
Chart: 
When the switch is re-connected as shown
Calculate Imax
Calculate the time constant t, L = 750 mH
On the graph show IL = 1.5 A after one time constant.
Sketch the voltage vs time graph for the above circuit.
On your graph show the coordinates with values for t and V
4
3
2
1
0
t (s)
IL (A)
Inductor
Imax
Exponential decay of current vs time t graph for an inductor with a 'make before break' switch
3 W
VS
Make before break switch
L = 750 mH
VL
3 W
VS
Make before break switch
L = 750 mH
VL

## Slide 11
Chart: 
Calculate Imax
4
3
2
1
0
t (s)
IL (A)
Inductor
Imax
Exponential decay of current vs time t graph for an inductor with a 'make before break' switch
2 Calculate the time constant t
3 W
VS
Make before break switch
L = 750 mH
VL

## Slide 12
Chart: 
4
3
2
1
0
t (s)
IL (A)
Inductor
Imax
Exponential decay of current vs time t graph for an inductor with a 'make before break' switch
3. On the graph show IL = 1.5 A after one time constant.
0.25
1.5
3 W
VS
Make before break switch
L = 750 mH
VL

## Slide 13
3 W
VS
Make before break switch
L = 750 mH
VL
Chart: 
Inductor
12
9
6
3
0
t (s)
V (V)
100%
67%
50%
33%
VL
4.4
5. On your graph show the coordinates with values for t and V
0.25
Exponential decay of volts V vs time t graph for an inductor with a 'make before break' switch
When the switch is connected as shown
4. Sketch the voltage vs time graph for the circuit.