## Slide 1
VS
L
C
R
At every instant, the generator / supply voltage: (VS = Vmsinωt) is given by:
VS = VL + VC + VR
IZ = IXL + IXC + IR
These relationships can best be shown on a PHASOR DIAGRAM
LCR Circuit

## Slide 2
R
C
L
I
RLC circuit
VL
VR
VC
I
ω
Phasor
Diagram

## Slide 3
See 6 RLC circuits applet

## Slide 4: LCR Circuit ~ Phasor Diagram
VL
VR
VC
I
ω
VR and I are IN PHASE
VL Leads I by 90o
VC LAGS I by 90o
Total reactance (XT) in the circuit is the difference between XL and XC (XL – XC or XC – XL)
XL- XC
XL
R
XC
R
Z

## Slide 5
VL
VR
VC
Vs
Ф
I
XT = XL- XC ie XL > XC
XT = XC- XL ie XC > XL
Phase angle between
Voltage supply and Current (or VR)

## Slide 6
Calculate the reactance of the capacitor
Calculate the reactance of the inductor
Determine the impedance of the circuit
RCL Circuits
This LCR circuit has a 5.0 Ω resistor in series with a 250 µF capacitor and a 15 mH inductor. The AC supply has a frequency of 50 Hz
15 mH
250 µF
5.0 Ω
50 Hz

## Slide 7
Calculate the reactance of the capacitor
RCL Circuits
This LCR circuit has a 5.0 Ω resistor in series with a 250 µF capacitor and a 15 mH inductor. The AC supply has a frequency of 50 Hz
2. Calculate the reactance of the inductor
15 mH
250 µF
5.0 Ω
50 Hz
correct sig.fig
correct unit

## Slide 8
XL = 4.7 Ω
XC = 13 Ω
8.3 Ω
5.0 Ω
9.7 Ω
R = 5.0 Ω
OR
OR

## Slide 9
Determine the supply voltage Vs(rms)
Determine the phase difference between the current and the supply voltage
RCL Circuits
This LCR circuit has a 5.0 Ω resistor in series with a 250 µF capacitor and a 15 mH inductor.
The AC supply has a frequency of 50 Hz that provides a current IRMS = 1.2 A
The reactance of the capacitor is 13 Ω, the inductor 4.7 Ω and the impedance of the circuit is 9.7 Ω
15 mH
250 µF
5.0 Ω
50 Hz

## Slide 10
Determine the supply voltage Vs(rms)
RCL Circuits
This LCR circuit has a 5.0 Ω resistor in series with a 250 µF capacitor and a 15 mH inductor.
The AC supply has a frequency of 50 Hz that provides a current IRMS = 1.2 A
The reactance of the capacitor is 13 Ω, the inductor 4.7 Ω and the impedance of the circuit is 9.7 Ω
2. Determine the phase difference between the current and the supply voltage
15 mH
250 µF
50 Hz
VR = 5 W
VC = 13 W
VL = 4.7 W
VX= 8.3 x 1.2
VR = 5.0 x 1.2
12 V
θ
By measurement
VS lagging current by 60º ± 2º
OR

## Slide 11
R
C
L
Example
VS = 110 V
f = 60 Hz
50 W
8 mF
0.8 H
What is the impedance
of the circuit?
b) What is the current in
the circuit?
c) What is the phase angle
between Vs and I ?

## Slide 13
Tweeter
Woofer