## Slide 1
Resonance review…
Mechanics - SHM

## Slide 2
Resonance ~Driven or Forced Harmonic Motion
Driving Force
If the driving force frequency matches the natural frequency…
then the amplitude will increase and can becoming large (and potentially dangerous). This is called Resonance.
When a system is disturbed by a periodic driving force and then oscillates, this is called forced oscillation. A system is said to have a ‘natural’ or resonance frequency ( fo ) which is independent of the frequency of the driving force.
Resonance frequencies will be explored in Waves (standing waves / harmonics) & AC Circuits (tuning radios).

## Slide 3
In physics, resonance is the tendency of a system to oscillate with larger amplitude at some frequencies than at others. At these frequencies, even small periodic driving forces can produce large amplitude oscillations.
Resonances occur when a system is able to store and easily transfer energy between two or more different storage modes (such as kinetic energy and potential energy in the case of a pendulum). However, there are some losses from cycle to cycle, called damping. When damping is small, the resonant frequency is approximately equal to a natural frequency of the system, which is a frequency of unforced vibrations.
http://en.wikipedia.org/wiki/Resonance
Notes: http://en.wikipedia.org/wiki/Resonance

## Slide 4
SHM of a Pendulum:
energy transformed from gravitational potential to kinetic energy and back again.
LC circuit:
Energy in the inductor could be considered analogous to kinetic energy, because it depends upon the current, ie the motion of the charge.
When that charge starts to "pile up" on the capacitor, it produces the electrical potential energy (cf gravitational potential energy).
SHM of a Spring:
energy transformed from spring potential to kinetic energy and back again.
Notes: ngsir.netfirms.com/englishhtm/Resonance.htm

## Slide 5
Resonance with capacitors and inductors
Resonance of a circuit involving capacitors and inductors occurs because the collapsing magnetic field of the inductor generates an electric current in its windings that charges the capacitor, and then the discharging capacitor provides an electric current that builds the magnetic field in the inductor, and the process is repeated continually. An analogy is a mechanical pendulum. In some cases, resonance occurs when the inductive reactance and the capacitive reactance of the circuit are of equal magnitude, causing electrical energy to oscillate between the magnetic field of the inductor and the electric field of the capacitor.
http://en.wikipedia.org/wiki/Electrical_resonance

## Slide 6
Assumes that the components are ideal, as assumed, the charge flows back and forwards for ever, with angular frequency wo,
Notes: http://www.animations.physics.unsw.edu.au/jw/LCresonance.html

## Slide 7
5mV
3mV
9mV

## Slide 8
An RLC circuit (or LCR circuit) is an electrical circuit consisting of a resistor, an inductor, and a capacitor, connected in series or in parallel. The RLC part of the name is due to those letters being the usual electrical symbols for resistance, inductance and capacitance respectively. The circuit forms a harmonic oscillator for current and will resonate in just the same way as an LC circuit will. The difference that the presence of the resistor makes is that any oscillation induced in the circuit will die away over time if it not kept going by a source. This effect of the resistor is called damping. Some resistance is unavoidable in real circuits, even if a resistor is not specifically included as a component. A pure LC circuit is an ideal which really only exists in theory.
There are many applications for this circuit. They are used in many different types of oscillator circuit. Another important application is for tuning, such as in radio receivers or television sets, where they are used to select a narrow range of frequencies from the ambient radio waves. In this role the circuit is often referred to as a tuned circuit.