## Slide 1
Electric Potential difference
(pd, V)
or
Voltage (V)
?
?
?
?
?
?

## Slide 3
Potential difference (Voltage), is the work done or the change in Electric Potential Energy per coulomb of charge
note 1V = 1JC-1
The symbol for Voltage is V and the unit is also V,

## Slide 5
The Monkey is doing Work to bring the +ve charges together
The Monkey is increasing the small +ve charge’s potential energy
0V
5V
20V
100V
1000V
How much work does the monkey do in bring a 1C charge from the 1st to 5th line?
How much work does the monkey do in bring a 1C charge from the 2nd to 4th line?

## Slide 7: Example:
It takes 6 Joules of work to move 2 coulombs of charge between 2 points in an electric field. What is the potential energy difference (voltage) between these 2 points?

## Slide 8
Roll of the Battery:
Supplies energy
Pumps the charge from – to + terminal
Maintains a ΔV across the external circuit

## Slide 9: Example:
If a battery cell provides 3.0 J of electrical potential energy in moving 2 coulombs of charge through the cell, what is the potential difference (or voltage) of the cell?

## Slide 10
Batteries provide potential difference between one end of the circuit and the other.
This difference in potential makes charges move.
The flow of charges is from high electric potential to low electric potential.

## Slide 11
Charges can “lose” potential energy by moving from a location at high potential (voltage) to a location at low potential.
Charges will continue to move as long as the potential difference (voltage) is maintained.

## Slide 12
Why aren’t birds on power lines shocked?
The Potential Difference between their feet is zero! (0 voltage)

## Slide 13
You're harmed only if current passes through part of your body. In order for that to happen, you must be touching two places that have a voltage difference between them. So the best way to avoid most dangerous situations is: Wear shoes with thick rubber soles, and keep one hand away from anything that conducts electricity. This makes it pretty difficult to get into a situation where current can flow into you at one place and out of you at another place.
One trick that electricians use is to keep one hand in their pockets when working with electrical equipment. If a zap occurs, it will flow from their working hand to the ground — not from hand to hand, passing right through the heart. You shouldn't be working with live electricity — ever! — but this trick of trade used by more advanced users shows how important it is to understand how electricity works and respect its authority.
Why do electricians work with one hand behind their back or in a pocket?
Notes: http://wiki.answers.com/Q/Why_do_electricians_work_with_one_hand_behind_their_back
http://www.dummies.com/how-to/content/avoiding-electric-shocks.html

## Slide 14: Question: Why is the ground prong longer than the other two in a plug?
Notes: the reason the ground (or earth) prong is longer is simply so that it is connected before the live prongs. That way if there is a short you know you are grounded before there is a circuit.
Reference https://www.physicsforums.com/threads/why-is-earth-pin-longer-than-other-two-in-a-plug-top.289956/

## Slide 15
Do you understand these diagrams?

## Slide 18
What is the change in potential energy of the electron in going from a to b?
What is the speed of the electron as a result of this acceleration?
Repeat both calculations for a proton.
Notes: Electron accelerated in TV picture tube. Example 17-2.