## Slide 1
Blocks 1 and 2 of masses ml and m2, respectively, are connected by a light string, as shown. These blocks are further connected to a block of mass M by another light string that passes over a pulley of negligible mass and friction. Blocks 1 and 2 move with a constant velocity v down the inclined plane, which makes an angle q with the horizontal. The kinetic frictional force on block 1 is f and that on block 2 is 2f.

## Slide 2
(a) On the figure below, draw and label all the forces on block ml.
m1g
N1
T
f
1 point for each drawn and labeled force

## Slide 3
(b) Determine the coefficient of kinetic friction between the inclined plane and block 1
1 point for correct substitution
of mg cos(q)
1 point for correct solution
1 point for expressing in terms
of the given quantities
Express your answers to each of the following in terms of m1, m2, g, q, and f.

## Slide 4
(c) Determine the value of the suspended mass M that allows blocks 1 and 2 to move with constant velocity down the plane.
Mg
f
2f
m1g
m2g
1 point for using Newton’s second law
1 point for correct weight components
1 point for correct friction terms
2 points for correct answer
Express your answers to each of the following in terms of m1, m2, g, q, and f.

## Slide 5
(d) The string between blocks 1 and 2 is now cut.
Express your answers to each of the following in terms of m1, m2, g, q, and f.

## Slide 6
(d) Determine the acceleration of block 1 while it is on the inclined plane.
m1g
f
1 point for correct friction in the equation
1 point for correct weight component
1 point for correct answer
Express your answers to each of the following in terms of m1, m2, g, q, and f.